## Slide 1: Trust Router Overview
IETF 86, Orlando, FL
Trust Router Bar BOF
Margaret Wasserman
mrw@painless-security.com

## Slide 2: Trust Router Draft
https://datatracker.ietf.org/doc/draft-mrw-abfab-trust-router/
Describes the role and purpose of a Trust Router
Defines the concept of communities
  COIs and APCs
Defines two protocols
  Temporary Identity (TID) Protocol
  Trust Router Protocol

## Slide 3: Trust Router Overview
Trust Router Operation
Communities
Temporary Identity Protocol
  Message contents
  Role of Trust Router as gateway
Trust Router Protocol
  Message contents
  Trust link types
Implementation Status

## Slide 4: Trust Router Operation

## Slide 5: Communities
Authentication Policy Communities (APCs)
  Used to authenticate access to RP Services
Communities of Interest (COIs)
  Group of RP Clients, IdPs and Trust Routers that share access to a set of services
  COI must be resolved to an APC (for a given IdP Realm), before authentication can be achieved

## Slide 6: Temporary Identity Protocol
Used by an RP to negotiate a Temporary Identity on a (set of) AAA Server(s) in a target realm
TID Request is sent to the RP’s local Trust Router and forwarded across a Trust Path to the target AAA Server(s)
Response is returned by reversing the Trust Path

## Slide 7: Temporary Identity Protocol
Simple request/response protocol
  Messages are encoded in JSON
  Uses GSS-API for authentication
Request include ½ of a DH exchange
Server replies with a list of AAA Server IP Addresses
  Response includes the other ½ of a DH exchange for each AAA Server
Both ends can compute a shared key that is used for the subsequent AAA authentication
  Key cannot be computed by intermediate Trust Routers

## Slide 8: Example TID Request
{"msg_type": "TIDRequest", "msg_body": {"rp_realm": ”mit.edu", "target_realm": ”oxford.uk.ac", "community": ”abfab-hackers.communities.ja.net", "dh_info": {"dh_p”: "FFFFFFFF…", "dh_g": "02", "dh_pub_key": "FBF98ABB…”} } }

## Slide 9: Trust Router as TID Gateway
Trust Router receives a TID Request from an RP Client (e.g. AAA Proxy)
Determines appropriate APC for the community included in the original request
  If different, moves original COI into orig-coi field
Finds matching rp_client entry (from gss_name), applies filters, and adds constraints to the message
Determines “Trust Path” and adds it to the message.
Forwards message to AAA Server (or next hop Trust Router)

## Slide 10: Trust Router Protocol
Runs between pairs of Trust Routers
  Configured as “peers” with GSS credentials to reach each other
“Routing” protocol used to dynamically distribute information about
  Available Trust Links
  Used to route TID requests and responses across the federation
  RP Client membership in COIs
  APC to use for each IdP Realm/COI pair

## Slide 11: Trust Link Types
Trust Link Types (named by target type)
  Routing Links
    Trust Router Link
      Indicates that the originating trust router can provide temporary IDs to reach the target trust router
    IdP Realm Link
      Indicates that the originating trust router can provide temporary IDs to reach the AAA servers in the target realm
  Information Flooding Links
    COI RP Membership Link
      Indicates that the the target RP Client is a member of the indicated COI
    APC Link
      Indicates that authentication for a target realm and COI should use the target APC

## Slide 12: Trust Path
A Trust Path is a set of Trust Links that forms a path across a federation between an RP and the AAA Server(s) in a Target IdP Realm
A Trust Path is valid for a given Community
Trust Routers forward TID Requests/Responses along Trust Paths, ultimately resulting in a TID that the RP can use to reach AAA Servers in the Target IdP Realm.

## Slide 13: Questions?